## Slide 1: CPU Caches
A rough overview

## Slide 2: Who am I?
Steve Humphries
  Principal Programmer (Low-Level / Platform / Graphics)
  Founder & Technical Director @ Compute Unit Limited
I’ve worked on a few different bits of HW over 30 years+
  ZX Spectrum, C64, BBC Micro, Atari ST, Amiga, PC, Raspberry Pi
  PS1, PS2, PS3, PS4, Xbox/360/One/X, Switch, Mobile
I’ve worked on a few games over the years in various roles
  TT Superbikes, MotorStorm 1/2/3, Driveclub, Onrush, Narcos, …

## Slide 3: CPU Cache
Who is this talk for?
  Programmers of all levels
Why does a programmer need to know about caches?
  Because they are key to extracting best CPU performance
How will this talk make my code better and faster?
  Hopefully a better understanding of how CPU uses data

## Slide 4: CPU Cache – Why?
CPU Clock Speeds improved faster than DRAM Speeds
CPU @ 4GHz = 0.25 nanoseconds (ns) per cycle
CPU cores can process 4-16 instructions / ns
DDR3 RAM latency worst case ~100ns / access (*1)
1 Instruction every 100ns is ~10 MHz CPU speed
Worst case wasting ~1600 CPU inst per 100ns RAM access
(*1) https://ece.uwaterloo.ca/~rpellizz/techreps/worstcaseanalysis.pdf

## Slide 5: CPU Cache – Why?
Consider wanting an apple from a lovely orchard in EU
  Every time you want an apple, you could drive/fly to the farm
  But that seems costly and time consuming
Instead, there is a supply chain for the apples
  Wholesaler buys tons of lovely apples from Farmer
  Store/Market requests crates of apples from Wholesaler
  You buy a box of apples from Store and place in fruit bowl

## Slide 6: CPU Cache – Why?
Each time you want an apple, you now do the following
Check in the fruit bowl for any apples (L1)
  Relatively quick as it’s in your house or apartment (<1 min)
Check local store/market for any apples (L2)
  Slightly slower, trip to local store (10+ mins)
Store/Market checks wholesaler centre for any apples (L3)
  A lot slower, road/rail involved (hours)
Farmer is requested to send lots of lovely apples (RAM)
  Much much slower, road/rail/shipping/airline (days)

## Slide 7: CPU Cache – Why?
Each stage of supply chain anticipates demand (prefetching!)
You notice apples running low so buy more before empty
Local Store/Market monitors sales (empty shelves is bad)
Wholesaler monitors demand (empty warehouse is bad)
Farmer tries to grow enough to meet demand, always selling
But sometimes, demand outstrips supply, bottlenecks/stalls

## Slide 8: CPU Cache – What?
Usually a Hierarchy of Cache Levels
Closest to CPU is typically, smaller, faster and more costly
Farthest from CPU is typically larger, slower and cheaper
Level1 (L1$) ~16KB - 32KB with ~5 Cycles / Access
Level2 (L2$) ~256KB - 512KB with ~25 Cycles / Access
Level3 (L3$) ~1MB - 4MB with ~50 Cycles / Access

## Slide 9: CPU Cache – What?
~32 KB
~5 Cycles
~1 KB
~1 Cycle
~512 KB
~25 Cycles
~2 MB
~50 Cycles
~16 GB
~500 Cycles
Reg
L1
L2
L3
RAM

## Slide 10: CPU Cache – Where?
CPU usually has 2 x L1 Caches
  Separate Caches for Instructions (I$) and Data (D$)
L1 I$ is Read-Only – Individual per CPU core
  Sometimes includes special logic for branches
L1 D$ is Read/Write - Individual per CPU core
  Usually supports more Reads than Writes per cycle
L2$ / L3$ is Read/Write – Could be shared by multiple cores
  Varies ‘inclusive/exclusive’ so will/won’t keep a copy of L1 I$/D$ or L2$

## Slide 11: CPU Cache – Where?
~2 MB
~50 Cycles
~512 KB
~25 Cycles
~32 KB
~5 Cycles
~1 KB
~1 Cycle
Core0
L1 I$
L1 D$
Core1
L1 I$
L1 D$
Core2
L1 I$
L1 D$
Core3
L1 I$
L1 D$
L2$
L2$
L3$
Registers
Registers
Registers
Registers

## Slide 12: CPU Cache – Where?
~256 KB
~15 Cycles
~2 MB
~50 Cycles
~32 KB
~5 Cycles
~1 KB
~1 Cycle
Core0
L1 I$
L1 D$
Core1
L1 I$
L1 D$
Core2
L1 I$
L1 D$
Core3
L1 I$
L1 D$
L2$
L3$
Registers
Registers
Registers
Registers
L2$
L2$
L2$

## Slide 13: CPU Cache – Where?
Core0
L3$
Core1
Core2
Core3
Core4
Core5
Core6
Core7
RAM
RAM
RAM
RAM

## Slide 14: CPU Cache – How?
Cache is divided into blocks – Cache Lines
  64B is the most typical size at present (2020)
  PS3 used 128B lines as do some current L3$ (Samsung)
Cache lines are organised in a 2D array [Sets][Ways]
  n-Sets = n-Lines / n-Ways
The ‘n-Sets’ is referred to as the cache ‘Associativity’
  This is usually tuned for each CPU architecture and cache Level

## Slide 15: CPU Cache – Prefetching
L1 and L2 usually have HW prefetchers
  Repeated access patterns/strides detected
  Most likely next cache line is pre-fetched in advance
  CPU usually has instructions for manual prefetching
  These should be used with care, can adversely affect perf
HW prefetchers can be a big performance win
  Usually takes 3-4 accesses before it kicks in
  Useful when doing long sequential runs over data

## Slide 16: CPU Cache – Associativity
Each level of cache may use different Associativity
  This is where Cache designers earn the $$$
Cache line lookup is partly indexed and searched
  Indexed using ‘Set’ and multiple ‘Ways’ searched
Each ‘Way’ is checked in parallel
  More ‘Ways’ can improve performance for certain access patterns

## Slide 17: CPU Cache - Associativity
32KB L1 D$ (8-Way Associative)
  32,768B / 64B = 512 Cache Lines
  8-Way means 8 x 64B Cache Lines / Set
  512 / 8 = 64 Sets (6-Bit Index)
512KB L2 D$ (16-Way Associative)
  524,288B / 64B = 8192 Cache Lines
  16-Way means 16 x 64B Cache Lines / Set
  8192 / 16 = 512 Sets (9-Bit Index)

## Slide 18: CPU Cache – 64-Bit Pointers?
x86-64 typically only uses 40-48 Bits of Address Space
  Some Server-class CPUs like Xeon use 56 bits
  Early versions of Windows 8 only used 36 Bits
Cache logic splits the 64-Bit address into chunks
  Upper 24/16 Bits of 64-Bit pointer are not used
  2-3 Bytes are pure zeros (wasted) on Desktop CPUs*
  Lowest 6-Bits (64B Line) are the offset into the Cache Line
  Middle Bits are used for Set, PageTable, VirtualMem indexing

## Slide 19: CPU Cache – 40/48 Bit Address Space
27 Bits
7 Bits
6 Bits
Tag
Set
Offset
40 Bits
35 Bits
7 Bits
6 Bits
Tag
Set
Offset
48 Bits

## Slide 20: CPU Cache – Logic
Extract the ‘Set’ index from 64Bit address
  (if Fully Associative) set = 0
Check for address match of all ‘n‘ Ways in the ‘Set’
  This is typically all done in parallel and is performance hotspot
  ‘Tag’ usually in separate array to save power / cycles
  (V)alid bit may be check before Tags
Page-Tables (TLB) and Virtual Memory lookups
  Could do whole other talk about these, but handled similarly

## Slide 21: CPU Cache – Logic
if (tagFound) CacheHit++
‘Way’ index is used to fetch Cache Line from Data RAM
LRU counter is updated
if (writingData)
  (D)irty Bit is updated

## Slide 22: CPU Cache – Logic
if (!tagFound) CacheMiss++
‘Way’ index is determined from Tag Data
  Is a Cache Line free? - Checks the (V)alid bit
  Else, LRU counter is checked to find line to Evict
  If (D)irty, evict Cache Line to next Cache Level or Main RAM
if (writingData)
  (D)irty Bit is updated, (V)alid Bit is updated, LRU is reset

## Slide 23: CPU Cache – Direct Mapped
1-Way with multiple Sets
  Cache Line is Directly indexed using the Set index
No searching of multiple ‘Ways’ is needed
  Much simpler logic, therefore usually faster/cheaper
Many addresses will map to the same Set/Way
  64KB Direct Mapped = 1024 Sets (10-Bit Index)
  Addresses spaced 64KB apart map to same Set
  1/1 Cache Lines are evicted per conflicted access

## Slide 24: CPU Cache – Direct Mapped
Set | Tag RAM (Way 0) | Data RAM (Way 0)
0 | Tag:V:D:LRU | 64B Data
1 | Tag:V:D:LRU | 64B Data
2 | Tag:V:D:LRU | 64B Data
3 | Tag:V:D:LRU | 64B Data
4 | Tag:V:D:LRU | 64B Data
5 | Tag:V:D:LRU | 64B Data
6 | Tag:V:D:LRU | 64B Data
7 | Tag:V:D:LRU | 64B Data
8 | Tag:V:D:LRU | 64B Data
9 | Tag:V:D:LRU | 64B Data
10 | Tag:V:D:LRU | 64B Data
11 | Tag:V:D:LRU | 64B Data
12 | Tag:V:D:LRU | 64B Data
13 | Tag:V:D:LRU | 64B Data
14 | Tag:V:D:LRU | 64B Data
15 | Tag:V:D:LRU | 64B Data

## Slide 25: CPU Cache – Fully Associative
n-Ways within single Set
  Cache Line is not indexed
  Searching of multiple ‘Ways’ is needed
  Complex logic, therefore usually slower/expensive
Any address will map to the same Set
  64KB Fully Associative = 1 Set with 1024 Ways
  1/1024 Cache Lines are evicted per conflicted access

## Slide 26: CPU Cache – Fully Associative
Set | Tag RAM Way 0 | Tag RAM Way 1 | Tag RAM Way ~ | Tag RAM Way n | Data RAM Way 0 | Data RAM Way 1 | Data RAM Way ~ | Data RAM Way n
0 | Tag Data | Tag Data | Tag Data | Tag Data | 64B | 64B | 64B | 64B

## Slide 27: CPU Cache – 4-Way Associative
4 Cache Lines per Set
  Cache Line is partly indexed using the Set index
All 4 ‘Ways’ are checked in parallel
  Balance of logic, therefore usually fast-ish/cheap-ish
Some addresses will map to the same Set
  64KB 4-Way = 256 Sets (8-Bit Index)
  Addresses spaced 16KB apart map to same Set
  1/4 Cache Lines are evicted per conflicted access

## Slide 28: CPU Cache – 4-Way Associative
Set | Way |  |  | 
0 | 64B | 64B | 64B | 64B
1 | 64B | 64B | 64B | 64B
2 | 64B | 64B | 64B | 64B
3 | 64B | 64B | 64B | 64B
4 | 64B | 64B | 64B | 64B
5 | 64B | 64B | 64B | 64B
6 | 64B | 64B | 64B | 64B
7 | 64B | 64B | 64B | 64B
8 | 64B | 64B | 64B | 64B
9 | 64B | 64B | 64B | 64B
10 | 64B | 64B | 64B | 64B
11 | 64B | 64B | 64B | 64B
12 | 64B | 64B | 64B | 64B
13 | 64B | 64B | 64B | 64B
14 | 64B | 64B | 64B | 64B
15 | 64B | 64B | 64B | 64B

## Slide 29: CPU Cache – Sequential accesses
Set | Way |  |  | 
0 | 64B | 64B | 64B | 64B
1 | 64B | 64B | 64B | 64B
2 | 64B | 64B | 64B | 64B
3 | 64B | 64B | 64B | 64B
4 | 64B | 64B | 64B | 64B
5 | 64B | 64B | 64B | 64B
6 | 64B | 64B | 64B | 64B
7 | 64B | 64B | 64B | 64B
8 | 64B | 64B | 64B | 64B
9 | 64B | 64B | 64B | 64B
10 | 64B | 64B | 64B | 64B
11 | 64B | 64B | 64B | 64B
12 | 64B | 64B | 64B | 64B
13 | 64B | 64B | 64B | 64B
14 | 64B | 64B | 64B | 64B
15 | 64B | 64B | 64B | 64B
0xC0DE0000
0xC0DE0040
0xC0DE0080
0xC0DE00C0
0xC0DE0100
0xC0DE0140
0xC0DE0180
0xC0DE01C0

## Slide 30: CPU Cache – Stride Accesses
Set | Way |  |  | 
0 | 64B | 64B | 64B | 64B
1 | 64B | 64B | 64B | 64B
2 | 64B | 64B | 64B | 64B
3 | 64B | 64B | 64B | 64B
4 | 64B | 64B | 64B | 64B
5 | 64B | 64B | 64B | 64B
6 | 64B | 64B | 64B | 64B
7 | 64B | 64B | 64B | 64B
8 | 64B | 64B | 64B | 64B
9 | 64B | 64B | 64B | 64B
10 | 64B | 64B | 64B | 64B
11 | 64B | 64B | 64B | 64B
12 | 64B | 64B | 64B | 64B
13 | 64B | 64B | 64B | 64B
14 | 64B | 64B | 64B | 64B
15 | 64B | 64B | 64B | 64B
0xC0DE0000
0xC0DE1000
0xC0DE2000
0xC0DE3000
0xC0DE4000
0xC0DE5000
0xC0DE6000
0xC0DE7000
Cache Line
Conflicts
Lines Evicted
Non-optimal
Cache Usage

## Slide 31: CPU Cache – Summary
Caches are built with 2 types of locality in mind
  Spatial and Temporal
Spatial
  Assumes that commonly accessed data is nearby
  Structures, Classes, Stack, etc
Temporal
  Assumes that the same/nearby data is accessed soon after earlier access
  Stack, common functions, loop counters, ‘this’ pointer, etc

## Slide 32: CPU Cache – Summary
Multiple levels of Cache
  Increasing in size and time to access
Cache misses are bad (L1), Bad(L2), BAD(L3)
  RAM is very far away in terms of CPU cycles
  CPUs can do a lot of work in those cycles
Knowing actual Cache sizes and layouts is useful
  Especially on fixed HW such as Consoles
HW Prefetching can be your friend
  Think in terms of 2-4 ‘streams’ of data accessess

## Slide 33: CPU Cache – Questions?